## Slide 1: Business Overview & Challenges
PCB designers send their design output package (in a zip file, sometime individual files) to fabricators to create a functional piece of hardware.
One of the biggest complaints from designers relates to quote response time from fabricators.
Many of the fabrication packages sent for quote are incomplete and require additional clarifications, technical discussions, and data files.
Back-and-forth interactions take time and become the largest contributing factor in delayed quotes.
The worst-case scenario is that a customer receives product that does not meet the design intent.

## Slide 2: Current State & Motivation
Sales person receives email from PCB designer for quote.
Sales person take a quick glance at the files, read any instructions from email and send the package to quote department.
Quote department then check each file in the package, do some sanity checks and repackage that into specific structure with some additional data and upload to CRM system and assign for engineers to further review the design files for manufacturability.
How can we automate the process so we can quickly validate the designer’s package and provide accurate quote within minimum time and minimal involvement of engineering staff.

## Slide 3: Pre-Quote Analysis Software
Pre-quote software is typically a quoting tool for managing and assessing the customer’s incoming PCB data files.
Can quickly tell if the PCB meets certain design rules.
This can include automatically checking required files and generating precise summary reports that identify potential risks.
These tools allow sales and quoting personnel, who typically do not have a technical engineering background, to work more independently from engineering and provide a highly accurate quote.
They are not intended to take the place of a full-blown computer-aided manufacturing (CAM) design rule check (DRC) tool.

## Slide 4: PCB Standards & Data Files
The industry standards for PCB types are:
  IPC-6012: Rigid Printed Boards
  IPC-6013: Flexible Printed Boards
  IPC-6018: High Frequency (Microwave) Printed Boards
  IPC-6012DS: Space and Military Avionics Applications
There are three different board classes as defined by IPC-6012 and IPC-6013.
  Class 1 is for “general electronic products” and is the lowest reliability class.
  Class 2 is for “dedicated service products” and requires a little more information to be provided.
  Class 3 is specified for the highest reliability and continued high performance in segments where equipment failure simply cannot be tolerated.
Netlists typically follow IPC-D-356, IPC-D-356A, or a mentor neutral file.
Common file formats are Gerber Files and ODB++ Files.

## Slide 5
PCB Design File Extensions
We need to add all supported file extensions.
 | ProtelAltium® | EAGLE | OrCAD™
Top Silkscreen | .gto | .plc | .sst
Top Soldermask | .gts | .stc | .smt
Top Copper | .gtl | .cmp | .top
Bottom Copper | .gbl | .sol | .bot
Bottom Soldermask | .gbs | .sts | .smb
Bottom Silkscreen | .gbo | .pls | .ssb
NC Drill File | .txt | .drd | thruhole.tap
Board Outline | .gm1 | .gko | 
Internal Layers | .gp1 | .g1 | 
Fab Drawing | .pdf | .pdf | .pdf
Readme | .txt | .txt | .txt

## Slide 6: File Requirements & Common Discrepancies
The file requirements will vary depending on the design.
What are different type of designs? -Single sided, with or without solder-masks, multi layered ?
PCB design software applications require the Drill file to be exported as a separate process from the rest of the design files, this is the most commonly forgotten file.
The Board Outline is another file that is often overlooked.This file can either be a stand-alone file, or be included within other layer files.
What are the common missing files you have experienced in past experiences?
Basic settings in PCB design - Units = Inches, Format = 2.3, Embedded Apertures = RS274X
Example. PCB noted as Class 3 but missing design requirements, such as minimum annular ring or clearance.
Example. Specified copper weights does not define whether they are prior to (base) or after (final) plating.
Example. Changing the design by increasing/reducing layers may change impedance requirement but not updated in the new drawings.

## Slide 7: Questions & Info needed
What other information you will gather from PCB designer other than zip file?
Can sales person input extra details about PCB designer’g needs along with sending zip file to quote?
What is the naming standard of files and how we can map extension of file to a particular type?
Can we get one sample zip containing all the files? We can explore if each file can be checked for certain properties?
Can we get the rules to relate file extension to a specific layer/design file?
Can we get the checklist that you follow for package validation?
What are the common issues your staff ( quote/engineering ) finds in the zip file from PCB designers?
Is there some information we can extract from readme file? Is it always provided?
One quote staff copied part number from one of the PDF file. Is that always the process? We have to check how we can read that in our software.
First level of validation - validate files by extension and check if all required files are provided according to the type of PCB design. Also need to check if the file actually is of the correct format based on the extension used in file name.
Next level of validation - Dig deep into each file to extract additional attributes that can give some useful information about design.